## Slide 1: SnapShotter: A lightweight Intrusion Detection for PLCs
Chenglu Jin, Saeed Valizadeh, Mason Ginter, and Marten van Dijk
Email: {chenglu.jin, saeed.val}@uconn.edu

## Slide 2: About us
Chenglu Jin
  Ph.D. Student at University of Connecticut
  Graduated from NYU Tandon (formerly known as NYU Poly)
  Hardware security and Embedded system security
  Physical Unclonable Functions, Hardware Trojans, Side Channel Analysis, Fault Injections, Secure Supply Chain Management, Secure Multi-party Computation, Secure Boot
Saeed Valizadeh
  Ph.D. Student at University of Connecticut
  System security
  Member of MACS (Modular Approach to Cloud Security) project
  Moving Target Defense, Intrusion Detection and Prevention System, SDN
Mason Ginter
  Member of CyberSecurity Club at Uconn
  Cyber Security and Programming

## Slide 3: Motivations
Industrial control systems are connected to the network, and therefore they are venerable to cyber attacks. E.g. Stuxnet targets SCADA systems.
Programmable logic controllers (PLCs) are one class of such devices mainly used for controlling the industrial processes.

## Slide 4: Adversarial Model
Malicious adversaries
  Have access to PLCs
  Can submit any malicious logic to the PLCs to generate arbitrary outputs from the PLCs to further hurt the industrial processes.
What the attacker cannot do:
  Physically tampering the PLC hardware

## Slide 5: Simple Idea
One Lightweight Intrusion Detection for PLCs can be:
Logging System
PLC
Monitoring Server
Logs
Integrity Protected Logs
SnapShotter Agent

## Slide 6: SnapShotter Agent
Stealthy logging mechanism with Forward Secure Key Management System.
The status of each PLC is logged and sent to a central monitoring server in a secure and stealthy way periodically.
The integrity of the logs can be verified by the server.
The adversary is not able to infer whether he/she gets caught or not, even when he/she compromised the device completely, including the logging mechanism and secret key.
If an intrusion is detected, the server will restart the infected PLCs with a known clean state. This will carry on the normal operation of the industrial processes.

## Slide 7: Logging Mechanism
Events?
Log(Time, Input, Output)
Encrypt Log by AES-128
Update Key by SHA-256
Period Ends?
Send Encrypted Logs to Server
Yes
Yes
No
No

## Slide 8: Assumption
Normal Operations
Compromise in progress
Malicious Operations
Compromise initiates
Compromise completes
Logging Mechanism Working
Logging Mechanism is Compromised
Logging gets compromised
Assumption: Some logs are generated between the beginning of the attack and the moment that the logging system gets compromised.

## Slide 9: Performance Overhead
Testing conditions:
  Running HelloWorld logic
  One period has 1000 scan cycles
  One event in each period
The average execution time of one scan cycle increases by 21.6%, comparing with the original OpenPLC design.

## Slide 10: Conclusion
We have implemented a lightweight intrusion detection system to secure PLC systems by using simple and practical techniques.
Security Guarantees: Guaranteed reports of malicious behaviors even when the logging mechanism and secret key are compromised.
Performance Overhead: 21.6% comparing with original OpenPLC
Please come to our demo.
Questions and thoughts are welcomed.